## Slide 1
4 3 2 1
4 3 2 1
4 3 2 1
4 3 2 1
5 4 3 2 1
3
2
1
4
5
Connector 1
1 11V - red
2 N.C
3 Button common - white
4 Ground - black
Connector 2
1 Flywheel motor
2 Feed motor
3 Flywheel button
4 Feed button
Connector 3
1 IR receiver - red
2 IR transmitter - white
3 N.C.
4 Ground - black
Connector 4 - Display
1 Ground - black
2 5V - red
3 SDA - white
4 SCL - white
Connector 5 – Rotary encoder
1 Ground - black
2 5V - red
3 SW - white
4 DT - white
5 CLK - white
Connector 6 - A2D
1 Ground - black
2 5V - red
3 SDA - white
4 SCL - blue
5 11V - purple
usb
Arduino Nano
5 4 3 2 1
6